## Slide 1: ESO’s Future Projects
Bruno Leibundgut

## Slide 2: European Southern Observatory
Mission
  Develop and operate world-class observing facilities for astronomical research
  Organize collaborations in astronomy
Intergovernmental treaty-level organization
  Founded in 1962; today 15 member states
  La Silla Paranal: VLT, VLTI, 3.6m, NTT, VISTA, VST
  Chajnantor: APEX and ALMA partnerships
  Armazones: ELT
  Paranal/Armazones: CTA-S
Headquarters in Garching and Office in Santiago

## Slide 3: European Southern Observatory

## Slide 4: ESO
Observatories La Silla and Paranal in operation 8 Telescopes, plus 4 telescopes for Interferometry
APEX in operation on Chajnantor
Atacama Large Millimeter Array (ALMA)
Public data archive
ESO Extremely Large Telescope under construction
Headquarters in Garching, Germany
Representation in Santiago de Chile
Joint ALMA Office in Santiago

## Slide 5
Paranal 2018
Paranal 2022

## Slide 6: Adaptive Optics Facility
GALACSI MUSE WFM offered
  GLAO to feed the MUSE Wide-Field Mode:
    seeing enhancer in 1x1 arcmin2 FoV @ 750nm
    4 LGSs located ≈1 arcmin from the optical axis
    No optics inserted in the MUSE scientific FoV
GRAAL + HAWK-I offered
  GLAO to feed HAWK-I camera
    seeing enhancer in 7x7 arcmin2 FoV @ 0.9 to 2.2
    4 LGS located outside the FoV
GALACSI MUSE NFW offered
  laser tomography adaptive optics (LTAO)
    full correction (goal 10% Strehl ratio) in 7.5x7.5 arcsec2 @ 650nm
    4 LGS located ≈ 8 arcsec from optical axis

## Slide 7: Four Lasers

## Slide 8: New VLT/I Instruments
GRAVITY – highest angular resolution in K-band
ESPRESSO – extremely stable high-resolution spectrograph
Matisse – mid-infrared interferometry instrument
ERIS – new NIR AO imager (NACO replacement)
  includes SINFONI upgrade
MOONS – high multiplex NIR spectroscopy
4MOST (VISTA) – high multiplex optical spectroscopy
Optical AO imager and spectrograph
FORS2 upgrade – maintain instrument operational
UV high-resolution spectroscopy

## Slide 9: ESPRESSO
The Echelle SPectrograph for Rocky Exoplanet and Stable Spectroscopic Observations
  ESPRESSO is a super-stable optical high-resolution fibre-fed spectrograph for the combined coudé focus of the VLT
  Uses any of the UTs or up to 4 UTs simultaneously
  0.38-0.8 μm
  R=120k-220k
  4UT R=60k
In commissioning

## Slide 10: MATISSE
Multi-Aperture mid-Infrared SpectroScopic Experiment
  VLTI four-telescope L, M and N-band imager
  Multi-axial beam combination, closure phase imaging
  Spectral resolutions between R=30 and 5000
  Operating with UTs and ATs
  Will use GRAVITY as a fringe tracker
Offered in P103

## Slide 11: CRIRES Upgrade
CRIRES Upgrade project
  1-5 microns spectral coverage, R~20k–100k
  Cross-disperser + new detectors will enlarge simultaneous wavelength coverage by ~10 times, will cover simultaneously one IR band
  Gas cells will provide few m/s radial velocity precision
  Polarimetric capabilities
  Refurbished AO system
Offered in 2019

## Slide 12: ERIS
SPIFFI Integral field spectroscopy
  FoV 0.8”, 3.2”, 8”; R~3000 & 8000; J‐K bands
NIX (camera)
  J‐K narrow/broad bands; 13/27 mas pix (26”/55” FoV)
  L‐M broad bands; 27 mas pix (55” FoV)
High contrast imaging
  Pupil plane coronagraph (L‐M)
  Focal plan coronagraph (L‐M)*
  Sparse aperture Masking (J‐M)
Long slit spectroscopy
  R=500, LM band simultaneously
Offered after 2020

## Slide 13: MOONS
Multi-Object Optical and Near-infrared Spectrograph
  Field of view: 500 arcmin2 at the 8.2m VLT
  Multiplex: 1024 fibers with the possibility to deploy them in pairs
  Medium resolution:
    Simultaneously 0.64μm-1.8μm
    R=4000–6000
  High resolution:
    Simultaneously 3 bands:
    0.76-0.90 at R = 9000
    0.95-1.35 at R = 4000
    1.52-1.63 at R = 20000
Offered after 2020

## Slide 14: 4MOST
4MOST will be a world-class facility for fiber-fed multi-object spectroscopy
  large field of view (> 4 deg2)
  spectral resolutions (LRM: R>5,000, HRM: R>18,000) for both Galactic and extragalactic applications
  high multiplex (1600 in LRM, 800 in HRM)
  broad wavelength coverage in LRM (400-885 nm)
  broad wavelength coverage in HRM (393-435 nm and 521-571 nm, 610-675 nm)
  implementation at the Cassegrain focus of the VISTA telescope
Offered after 2022
Community workshop 6-8 May 2019

## Slide 15: Visible Adaptive Optics Instrument
VISIBLE MCAO
  Maintain optical imaging at the level of HST into the next decades
  Strong synergies with ELT
Optical camera
  ~7 mas per pixel
  30 arcsec diameter FoV
  Focus on VRI but also UBz sensitivity
IFU Spectroscopy
  ~3x3 arcsec2 FoV
  Spec. res. at R~5000
Adaptive Optics
  Diffraction limited in V-band (AOF + 2 more DMs)
  Strehl ratio >10% in V-band
  4 or 5 Lasers
  Near IR WFS

## Slide 16: OIR Future Strategies
Flexibility
  Astrophysics covers many topics and techniques
  Completeness of instrumentation
  Reaction to interesting new events, object and topics
Coordination
  Instrumentations programmes at different facilities
    either through a large pool or through collaboration between observatories
  Planning between ground and space
  Time allocation between observatories
Operations
  inbuilt flexibility
  archive  open distribution of data

## Slide 17: La Silla beyond 2020
Dedicate large telescopes to specific science topics
  3.6m telescope: exo-planets, radial velocity studies
    HARPS; NIRPS
  NTT: transient sky
    EFOSC2, SOFI, (ULTRACAM); SOXS
Hosted telescopes
  in operation upcoming
    2.2m MPG TBT
    1.54m Danish BlackGEM
    1.2m Euler NEOSTEL
    REM
    TAROT-S
    TRAPPIST
    ESO 1m
    ExTra
    MASCARA

## Slide 18: NIRPS
NIRPS @ 3.6m : High Accuracy NIR Spectrograph
  NIR (970-1800 nm)
  High Resolution: R>80000
  AO-Assisted
  Simultaneous observations with HARPS

## Slide 19: SOXS
SOXS @ NTT
  Broad-band spectrograph, 350nm through 2.0μm
  R ~ 4,500 (3,500–6,000)
  Two arms (UV-VIS + NIR)
  S/N ~ 10 spectrum, 1-hr exposure at R ~ 20
  Acquisition camera (3’x3’) to perform photometry in ugrizY
IR
Vis

## Slide 20: ALMA
Observe the cold universe
  wavelengths from 300μm to 1.3mm (1 THz to 200 GHz)
Global Partnership
  Europe (ESO), North America (USA/NSF and Canada/NRC), East Asia (Japan/NINS, Taiwan/NSC/ASIAA, South Korea/KASI)
66 antennas located at 5000m altitude
  50 12m antennas
  12 7m + 4 12m antennas (compact array)

## Slide 21: The ALMA Revolution
Increased sensitivity, higher angular resolution

## Slide 22: ALMA Receivers

## Slide 23: ALMA Plans
Defined in the roadmap
Increase receiver bandwidth
  Increased survey speed
Improve archive capabilities
Longer-term plans
  Increase maximum baseline
  Focal plane arrays
  More 12m antennas

## Slide 25: ELT - ESO’s next large telescope
~52 m (Horizon)
54 m

## Slide 26: ELT

## Slide 27: ELT Design
5 mirror telescope with 798 hexagonal segments making up the 39-m primary mirror

## Slide 28: ELT Instrumentation Programme
METIS
Mid-IR imager and spectrograph
HARMONI
Integral Field Spectrograph
MICADO+MAORY
Imager and single slit spectrograph
HIRES
High resolution spectrograph
MOSAIC
Multi-object spectrograph
Second generation instruments (completed Phase A)
PCS
Extreme AO imager and spectrograph

## Slide 29: HARMONI Integral-field spectrograph
3D spectrograph (IFU) covering optical (0.47 μm) to NIR (2.45 μm)
Resolving power R=3500 - 20000
32000 spatial pixels
From seeing limited down to the diffraction limit with SCAO and LTAO
Range of spatial scales with field of views from 9”x6” to 0.8”x0.6”
Integral Field Spectrograph
Natural Guide Star System
Relay optics
Laser Guide Star System
IFS rotator and cable wrap
IFS electronics

## Slide 30: MAORY
Multi-conjugate AO system using 6 laser guide stars and 3 natural guide stars
1 or 2 deformable mirrors in addition to ELT M4 to correct atmospheric turbulence over 120arcsecs field of view

## Slide 31: MICADO
Imaging from 0.8-2.4µm, > 30 filters, an array of 3x3 detectors with 4096x4096 Pixel scales of 4mas (field of view ~53”) and 1.5mas (FoV ~20”)
Astrometric imaging to 50µarcsec precision across whole image
Spectroscopy for single compact objects, two settings (0.8-1.4µm and 1.5-2.4µm) at spectral resolving power ~8000.
Coronagraph plus single conjugate AO
Time Resolved Astronomy as fast as 4mas

## Slide 32: METIS
METIS covers the thermal / mid infrared wavelength range from 3µm to 19µm
  All observing modes diffraction limited. SCAO
Imaging at L,M, N, Q bands: FoV 10”x10”
Low resolving power spectroscopy
  R ~ few 102-103, slit spectroscopy, LMN bands
  High resolving power (R ~ 100,000) IF spectroscopy at L,M-band, FoV 0.5”x0.5”
  GOAL: High resolving power N-band IFS
  Coronagraphy for high contrast imaging
Warm Cal Unit
METIS cryostat
Imager
LM IFU
Spectro.
AO WFS

## Slide 33: Instruments on Nasmyth A
MAORY/MICADO
METIS
HARMONI

## Slide 34: Phase A studies
HIRES
  High spectral resolving power (R>100000)
  Optical to near infrared
MOSAIC
  Multi-object spectrograph
  Optical to near infrared
  Single object and multi-IFU