## Slide 1: PSIM code training
J. Kolb, 10/12/12
(Background: Modal Pseudo-Synthetic Interaction Matrix for the AOF)
Notes: <number>

## Slide 2: PSIM code
Dedicated code for Pseudo-Synthetic IM (PSIM) generation
Relies on a model
Incorporates measured parameters
Pseudo-synthetic interaction matrix modeling
10/12/2012
<number>
PSIM code training, ESO
Notes: <number>

## Slide 3: “Pseudo-synthetic IM” - code -
10/12/2012
PSIM code training, ESO
<number>

## Slide 4: “Pseudo-synthetic IM” - code -
10/12/2012
PSIM code training, ESO
1170 Influence Functions (FEA) or stiffness modes, or System modes
Shack-Hartmann model (geometric or diffractive, with or without noise) 40x40 sub-apertures (1240 valid)
Interaction Matrix
Mis-registrations: x & y shifts, rotation, x & y stretches of WFS w.r.t. DM
<number>
Notes: <number>

## Slide 5: “Pseudo-synthetic IM” - DM model -
10/12/2012
PSIM code training, ESO
DM model includes:
  DSM Influence Functions generated by Finite Elements Analysis, and extrapolated to a square grid (240x240 pixels for geom WFS model, 720x720 for diffractive)
  After DSM installed on ASSIST: real Influence functions as provided by interferometric measurements
  Possible use of the basis of stiffness modes of the mirror
  Mis-registration errors: x/y shifts, rotation, x/y stretch
  Exact pupil shape accounting for the finite surface of the DSM
<number>

## Slide 6: “Pseudo-synthetic IM” - WFS model -
10/12/2012
PSIM code training, ESO
WFS model includes
  Geometric or diffractive model
  Detector simulation including Read-out and Dark noises, biases, charge diffusion…
  Various centroiding algorithms: CoG, wCoG, Correlation.
Inputs:
  AOF SHWFS characteristics: number of sub-apertures, FoV, number of pixels, detector characteristics
  Source size (extended source is often used to record Interaction Matrices)
<number>

## Slide 7: PSIM WFS display
Spot display also in geometric model
Slopes
10/12/2012
<number>
PSIM code training, ESO
Notes: <number>

## Slide 8
PSIM code training, ESO
Emulates full detection chain. Inputs:
  Number of photons (for photon noise)
  Exposure time
  Quantum Efficiency
  PSF (charge diffusion factor)
  Dark current
  Detector saturation level
  Detector conversion factor (microvolts per electron)
  Detector Bias voltage
  Excess noise (for Electron Multiplying CCDs)
  Read-Out Noise
  ADC gain (electrons per ADU)
PSIM – WFS model – Detector
<number>
10/12/2012

## Slide 9: AOF PSIM
X slopes
Y slopes
Actuators
Influence of actuators limited to a few sub-apertures
10/12/2012
<number>
PSIM code training, ESO
Notes: <number>

## Slide 10: AOF PSIM
10/12/2012
<number>
PSIM code training, ESO
Notes: <number>

## Slide 11: Application: Closed loop with PSIM
10/12/2012
<number>
PSIM code training, ESO
Notes: <number>

## Slide 12: Application: Closed loop with PSIM
10/12/2012
<number>
PSIM code training, ESO
Notes: <number>

## Slide 13
10/12/2012
PSIM code training, ESO
Mis-registration create instability at the inner and outer edges of the pupil.
<number>

## Slide 14
PSIM code training, ESO
MAD tests
10/12/2012
SCAO, Nb of modes filtered
Nb modes filtered
Closed loop Strehl
 PSIM gives better performance than measured IM, and this over a larger range of modes filtered (thus more robust to atmospheric conditions)
PSIM
Measured on fiber
Verification that for measured IM, 20 modes filtered is the optimum (this value has been used for 5 years)
<number>

## Slide 15
PSIM code training, ESO
MAD tests
10/12/2012
IM comparison
Loop gain
Closed loop Strehl
Very similar performance.
PSIM = IM fiber > IM turb
Measured on turbulence
Measured on fiber
Synthetic
PSIM > IM fiber > IM turb
PSIM includes mis-registration (see 1.9.1)
<number>

## Slide 16: Identification by projection of IMs
Estimation from measured IM
Simple projection of the IM difference IM*-α0IM0 on the sensitivity IMs gives the mis-registration parameters
10/12/2012
<number>
PSIM code training, ESO
Notes: <number>

## Slide 17: Mis-registration: example
Measured on fiber
10/12/2012
<number>
PSIM code training, ESO
Notes: <number>

## Slide 18: It works!
Y shift
X shift
Rotation
10/12/2012
<number>
PSIM code training, ESO
Notes: <number>