## Slide 1: METIS
Christoph Haupt (PM)
Ralf Siebenmorgen (PS)

## Slide 2: METIS
    Ongoing Science Updates
    Ralf Siebenmorgen (PS)
Notes: METIS architecture did not change, therefore you see the same picture as last time.

## Slide 3: METIS Observing Capabilities
3 – 19 μm imaging at:
  low/medium resolution slit spectroscopy
  coronagraphy for high contrast imaging
3 – 5 μm IFU spectroscopy (R~105)
  + mode with extended instantaneous wavelength coverage
Reach diffraction limit by applying SCAO
Notes:   Imaging at L/M band: The imager shall include low/medium resolution (R ~ few hundred - thousand) slit spectroscopy as well as coronagraphy for high contrast imaging.
  Imaging at N/Q band: The N-band imager shall include low/medium resolution (R ~ few hundred - thousand) slit spectroscopy as well as coronagraphy for high contrast imaging.
  High resolution (R ~ 100,000) IFU spectroscopy at L/M band, including a mode with extended instantaneous wavelength coverage.
  GOAL: High resolution IFU spectroscopy at N band. Not in the baseline design.

## Slide 4: Imaging Sensitivity
λ | F | mag
L | 1 μJy | 21.2
M | 10 μJy | 18
N | 100 μJy | 14

## Slide 5: Spectroscopic Sensitivity
IFU point source spectroscopy of unresolved lines at R=105

## Slide 6: Ongoing Science Updates
Oct.’17: Baseline Instrument
Jan.’18: Verfication of baseline
Mar’18: Re-simulation of science cases
Mai’18: Science Update@PDR
Milestones

## Slide 7: Technical items
ADC
Coronagraphy
LTAO
NQ band detector

## Slide 8: Ongoing ADC Simulations
no ADC
fixed ADC
ideal ADC
intensity1/4 stretch
PSF at airmass 1.6 simulated for ADC optimized to airmass 1.4
Fixed vers movable ADC:
higher throughput, less ghosts, higher TLR

## Slide 9: Coronagraphy Concept M. Kenworthy, O. Absil
Ring-Apodized Vortex Coronagraph (RAVC) + prevents star light reaching detector - sensitive to jitter (<1mas), needs several optical elements spread over instrument
Apodized Phase Plate Coronagraph (APP) + robust (1 optical element), insensitive to jitter - 10- 3..4 of light reach detector (saturation)

## Slide 10: Coronagraphy
Contrast
Separation (arcsec)
Spec

## Slide 11: LTAO
“Laser guide stars for good sky coverage”
METIS LTAO is not foreseen in ELT Instrumentation Roadmap
No funding available in the foreseeable future (~2035)
Provision for LTAO comes at significant cost (PFS design, mass dummies, WSS construction, …)

## Slide 12: LTAO
Impact:
Extragalactic science
Asteroids
Faint Brown-Dwarfs
Faint (T Tauri) protoplanetary disks
CRE might be submitted
(Management process see CH talk)

## Slide 13: NQ band detector
Aquarius: 20yr old device, designed for space and manufactured for ground with wrong coating

## Slide 14: NQ band detector
Aquarius lab test by Salima Mouzali

## Slide 15: NQ band detector
GeoSnap lab test:
Outside ESO
M. Meyer in the US by ~ April 2018
Aquarius lab test by Salima Mouzali

## Slide 16: Phase A Science

## Slide 17: Ongoing Science Updates
Most significant developments since phase A: exoplanets have become science drivers  high contrast imaging (HCI)
Both direct imaging and high resolution spectroscopy require HCI  coronagraphs
HCI drives requirements on optical system, opto-mechanical stability, and pupil alignment

## Slide 18: Observing Modes

## Slide 19: Observing Modes

## Slide 20: Observing Modes

## Slide 21: Ongoing Science Updates

## Slide 22: Direct imaging of Debris Disks
1 hr integration time
Disk model by Lebreton+(2015)
Ftotal ~ 10 mJy @ L 300 mJy @ N
Central star not included
L band (~3.5 μm)
N band (~10 μm)
METIS will probe dust distribution in rocket planet region of bright, warm debris disks and explore exo-zodiacal light
Simulations of debris of ηCrv

## Slide 23: Direct imaging of Proto-Planetary Disks
METIS will resolve rings, gaps, and embedded planets
Inner (7AU) CO gas disk
(CRIRES spectro-astrometry Pontoppidan et al. 2008)
METIS IFU simulation CO @ 4.7 μm
SR21 transitional disk
Outer dust disk (ALMA, Pinilla et al., 2015)

## Slide 24: Direct imaging of Proto-Planets
Proto-planet around HD 100546 (Quanz+ 2013, 2015)
METIS at 9µm
VLT NACO APP @ L-band
HST/ACS F435W
@ M-band

## Slide 25: Exoplanet Discovery Space
Direct imaging
Radial velocity
Transits
Microlensing
Solar System
V
Pepe, Ehrenreich & Meyer (2014)
Notes: Annahmen: Simulation von einem 100 M-Sterne Survey
den Planeten liegt eine log-normal Verteilung des Abstands zugrunde

## Slide 26: Exoplanet Discovery Space
Pepe, Ehrenreich & Meyer (2014)
simulated survey of 100 M-stars; planet separation assumed to have a log-normal distribution.
METIS detection probability 95%
Exoplanet discovery space
Notes: Annahmen: Simulation von einem 100 M-Sterne Survey
den Planeten liegt eine log-normal Verteilung des Abstands zugrunde

## Slide 27: Earth-like planet around α Cen A
What would a habitable Earth around Alpha Centauri look like?
real Earth spectrum 
METIS filter used in simulation
Image of the Earth at α Cen 
(full end-to-end simulation, 5 hrs)

## Slide 28: Earth-like planet around α Cen A
2 planets radii of 1 REarth
at 0.5 AU (400 K) and 1 AU (280 K)
albedo = 0.3
L (αCenA) = 1.52 LSun
Contrast:
L~ 3×10-9, M~ 2×10-8, N~ 5×10-5 (inner planet)
N~ 1×10-7 (outer planet)
tint ~ 2h

## Slide 29: Planets around α Cen A
Planet at 0.5AU detected in L,M,N
Planet at 1 AU detected only in N

## Slide 30: XXL Contrast
High Contrast Imaging (HCI)
combined with
High Dispersion Spectroscopy (HDS)
(Snellen+, Nature 2014)

## Slide 32: Exoplanet Atmospheres
What would a habitable Earth around Alpha Centauri look like?

## Slide 33: HCI + HDS  XXL Contrast
Simulation of HDS+HCI observations of
a planet orbiting α Cen A
(XXL ~ 10-10 TBC for METIS)

## Slide 34: HCI + HDS  10–10 Contrast
Assumptions:
Tstar = 5800 K
Rstar = 1.22 RSun
dist = 1.34 pc
Rplanet = 1 – 1.5 REarth
Dplanet = 0.6 – 1.2 AU
Tplanet = 255 – 355 K
ABond = 0.3
vplanet = 60 km/s
Earth-like atmosphere
CO bands @ 4.82 – 4.89µm
 S/N ~ 8 in 30 hr
0.7
Method applicable to many more planets closer in

## Slide 35: Observing Modes
Mode | Band | Config | Science Driver
Imaging | LM | direct | Circumstellar structures: Debris+Protoplanetary Disks, Proto-Planets, YSO, evolved stars
 |  | APP | Exoplanets: search + characterization
 |  | RAVC | 
 | NQ | direct | Circumstellar structures: Debris+Protoplanetary Disks, Proto-Planets, YSO, evolved stars
 |  | APP | Exoplanets: search + characterization
 |  | RAVC | 
Longslit Spectroscopy | LM | full band | Chemistry + Ices: Water, CO, Methan
 | NQ | full band | Exoplanetary atmospheres:solid-state mineralogy and chemistry in YSO and evolved stars
 |  | [SIV] & [NeII] | Circumstellar environments
Integral-field Spectroscopy | LM Dλ=50nm | direct | Kinematics and chemistry of circum-stellar environments
 |  | APP | Exoplanets: “Snellen” technique
 |  | RAVC | 
 | LM Dλ=300nm | direct | Line studies of gaseous environments (+ISM)
 |  | APP | Exoplanets: “Snellen” technique for known targets
 |  | RAVC | 
Pupil Imag. | L | diagnostic | Calibration
 | N |  | 

## Slide 36: METIS
    Consortium News

## Slide 37: METIS Consortium
Notes:   Imaging at L/M band: The imager shall include low/medium resolution (R ~ few hundred - thousand) slit spectroscopy as well as coronagraphy for high contrast imaging.
  Imaging at N/Q band: The N-band imager shall include low/medium resolution (R ~ few hundred - thousand) slit spectroscopy as well as coronagraphy for high contrast imaging.
  High resolution (R ~ 100,000) IFU spectroscopy at L/M band, including a mode with extended instantaneous wavelength coverage.
  GOAL: High resolution IFU spectroscopy at N band. Not in the baseline design.

## Slide 38: METIS Consortium May 2017
Notes: May Consortium meeting Paris

## Slide 39: METIS Consortium News
Warm Calibration Device WCU: Proposal from “Universität zu Köln” UzK was approved.
Portuguese institutes took over warm support structure and is called CENTRA.
ETH: Search for successor for M. Meyer at ETH is ongoing. Reorganisation of Astronomical Institute took place.
N-band spectrometer study proposal submitted. Selected and high ranked for the next project phase. Not started yet due to major programme review. Expected (hoped) start beginning of 2018.
PDR date fixed (14 May 2018) and chairperson (Andreas Glindemann) selected.
MOU has been signed (except by A*)
Interaction ESO / consortium intensifying on engineering aspects.
METIS considering to prepare a CRE for the LTAO.

## Slide 40: METIS
    METIS Design Status

## Slide 41: Warm Support Structure
  Lower structure which interfaces with Nasmyth platform is rigid.
  Cryostat alignment structure CAS connects to the elevation ring.
  Design is still being iterated
  LTAO is a driver of the WSS
  FEA started
  Mass WSS ~ 8t
Notes: Specification for the alignment structure still to be worked out
Depends on pupil stability which is crucial for HCI

## Slide 42: METIS Optical Overview
SCA
SCA PP1:
Field Selector
CFO
Optical Overview
CFO PP1: masks,
CFO-CST
E-ELT Focal Plane
CRY-
WIN
Dichroic
IMG-LM FP1: Detector
(LM)
(NQ)
IMG-NQ FP1: Detector
IMG-NQ PP1:
Filters, Lyot, APP
Collimator
LMS PP4: Main Dispersion
LMS FP4:
Detector
LMS PP3: Pre
Dispersion
IFU
LMS
Spectral
IFU
IMG
CFO-AOP
De-rotator
CFO-K1, K2, K3
CFO FP1
CFO PP2: CFO-CHO
CFO FP2:
Mask / vortex
LMS
PP1:
Mask
WCU FP1
SCA FM1
IMG-LM PP1:
Filters, Lyot, APP
LMS FP3:
Mask
IFU
(LMS FP1, PP2, FP2)
LMS
pickoff
LTA
LTA LGS
Lenslet array
Detector (6x)
Zoom
optics
LTA Fold
Mirror /
Dichroic
NGS
Lenslet
Detector
(3x)
CFO-CM1
CFO-FM1
CFO-CM2
CFO-CM3
CFO-
FM2
CFO-FM3
CFO-CM4
CFO-CM5
CRY
LU1
LU2
SCA PP2:
Modulator
Filters
SCA FP2:
Pyramid
SCA PP3:
Detector
LU3
PIL
PIL
Analyzing optics
Movable point-sources (WCU FP2)
WCU
Integrating Sphere
(WCU FP2)
WCU PP1
Mask(s)
Autocollimator (WCU FP2)
SCA FP1
SCA FM2
Notes: METIS architecture did not change, therefore you see the same picture as last time.
Pupil stability mirror was added. Requirements not clear. What is clear
Pupil stability requirements to be done

## Slide 43: METIS Cryostat
Notes: Cryostat design progressed further
Manufacturability and maintenance taken into account
Thermal layout started and temperatures chosen
ETH engineering office started design work in iteration with manufacturing company
KASKAG. The involvement of KASKAG is on a consultant level where questions
concerning feasibility, standard components and processes and practical aspects are
answered.
(Thermal layout for Geosnap does also exists and T are higher)

## Slide 44: METIS Subsystem Packaging
LMS
NQS
IMG
SCA
CFO-top
derotator
CCS
Notes: METIS architecture did not change, therefore you see the same picture as last time.

## Slide 45: METIS “Skeleton” Design
  “Skeleton Model” created.
  Based on CAD model and interfaces.
  Ensure that interfaces stay aligned at vacuum and thermal loads. Can also be linked to Zeemax
Notes: Another aspect of the CFO that made progress in Q3 was the ‘skeleton’ CAD model and the CFO packaging concepts. As mentioned in the previous report, the skeleton model plays a key role in planning manufacturing and alignment at ambient temperature which ensures optical accuracy and tolerances when at cryogenic operating temperatures. The skeleton now includes instrument temperatures to be used during operations as well as current materials choices for the various components. The skeleton is then ‘warmed up’ to ambient temperatures to ensure correct sizing for the cryostat development. Moreover, a set of common coordinate systems is now in place such that all subsystem partners can properly align shared CAD models. The CFO skeleton model is shown below as well as the model shown within the latest METIS packaging concept.

## Slide 46: METIS SE and CFO
System Engineering
  Requirements breakdown and allocation was done and data base was populated. System Requirements Review took place.
  Pupil stability has been further analyses.
  Mass budget was updated. Estimate is 18t instead of 9t.
Common Fore Optics
  Optical design frozen for PDR. Pupil stabilization mirror was added (FM2). Tolerance analysis was done.
  Start CM4 or CM6 prototyping before PDR
Notes: Common for optics.
A more detailed tolerance analysis was done for the CFO. The following parameters were investigated: wavefront error, back focal length, boresight error, exit pupil piston and decenter both at FP1 and FP2 locations
A draft AIV plan was established for the CFO.
CFO mechanical
Evaluations on which materials to choose for a potential prototype are being finalized and initial planning efforts
This goal is to start on the prototype effort in Q4 with material purchase, machining of the blank and start polishing
Chopping

## Slide 47: METIS SCAO
Pyramid WFS selected
  Design, interface and technology research started.
Optical design frozen for PDR
Mechanical Design
  Iterations are ongoing
Modulator
  Procurement specification written and potential supplier contacted.

## Slide 48: METIS Imager
Change of CFO FoV required redesign of Optics
Optical design frozen for PDR
Temperatures have been agreed with ETH.
Concern:
  Q-band: dichroic and temperatures
  Cryo-mechanisms delivery schedule
  NQ-band science detector
  Heat dissipation of NQ band motors.

## Slide 49: Mechanisms, Instrument Control
Documentation completed to launch procurement of components for prototyping an ICAR mechanism
JWST MIRI test bench refurbished to enable ICAR tests before PDR
Initial code tree set up, defining METIS observing modes in python.
Good progress on IMG and LMS cabinet layout detailing PLC and mechanisms sub-racks.
Control breadboard with hardware-in-the-loop and simulation modes.
Notes: ICAR: Indexed Cryogenic Actuator for Rotations
The present baseline is to equip METIS with 14 to 17 ICAR mechanisms,

## Slide 50: METIS 3 main risks
NQ-band detector performance and availability
  Baseline is the Visir Aquarius with known problems.
  Impossible to set up consortium for procuring improved Aquarius detector.
  MCT detector GEOSNAP from Raytheon identified as alternative. Detector was procured by M. Meyer and tests should start in May 2018 at University of Arizona.
Staying within allocated financial budget
  Closely monitor the cost and identify down-scope options
Calibration of the ELT thermal background
  Study Visir data
  Develop calibration schemes

## Slide 51: METIS last 6 month
Populate the requirements platform “Polarion”, Complete the system requirements breakdown and allocation to sub-systems, and do the System Requirements Review: Data base populated and SRR was done.
Perform the N-band spectrometer study: Study proposal N-band spectrograph submitted. Highly ranked. Delayed due to Break Through Initiative program review. Start expected begin 2018.
Deliver METIS background flux levels to detector group: Flux levels were delivered.
Investigate realistic N(Q) band detector options: AQUARIUS remains baseline. MCT detector procurement ongoing and tests will start in May at University of Arizona.

## Slide 52: METIS last 6 month
Define if PSF reconstruction is a requirement: Still to be done.
Handover WPs to Portuguese institutes: Warm Support Structure handed over and good progress has been made.
Continue with the WCU design work: Proposal was approved in Spring and funding for all phases secured. Work continued.
Analyze Q-band performance: Q-band is an objective. Only 4% transmission. Drives the thermal design. In case MCT detector will be selected for NQ-band imager Q-band will disappear.
Continue with the design of all subsystems: Good progress has been achieved of the subsystems design.

## Slide 53: METIS next 6 month (to PDR)
Begin with the N-band spectrometer study.
Procure the MCT detector for the N band imager and prepare for the test.
Decide how to proceed with METIS LTAO.
Complete the METIS preliminary design work and document it.

## Slide 54: METIS
Thank you

## Slide 55: METIS
Backup

## Slide 56: METIS

## Slide 57: METIS