## Slide 1
High Acuity Wide-field K-band Imager
λ range: 0.85 - 2.5 m
field: 7.5‘ x 7.5’ with 0.1” pixel
filters: VISTA: z,J,H,Ks ; narrow band:
Brγ, CH4, H2, 1.061, 1.187, 2.090 m
detectors: 4 Hawaii 2k at 60-80 K
design: all reflective at 120K
sensitivity: 21.6 [mag/10σ/1h] in K
spatial resolution: <0.4’’ (FWHM) with AO
HAWK-I

## Slide 2
•4 Lasers
•Deformable thin-shell secondary mirror with 1070 actuators
•WFS modules
The Adaptive Optics Facility

## Slide 3
GRound layer Adaptive optics Assisted by Lasers
GRAAL

## Slide 4
+ GLAO
seeing
HAWK-I with GRAAL
Gain in:
sensitivity
resolution
1.2
0.8
0.4

## Slide 5
HAWK-I with GRAAL:
+ resolution <0.4’’ (FWHM) uniform over 7.5’x7.5’
+ 0.5mag sensitivity gain
+ exposure time reduced by ~2
Galaxy Cluster at z~1.5, FWHM~0.3” in K
courtesy C.Lidman