## Slide 1: IFW PLC Libraries
Dan Popovic

## Slide 2: Topics
Function/Device Control Concept
ELT PLC Library Concept
OPC UA Interface
Logging
Device Simulators
GUI Templates
State Machine Concept
Data model
Integration with the Instrument Control Software
Overview of Supported Functionalities

## Slide 3: Documentation
ELT ICS Function Control Framework (FCF) https://www.eso.org/projects/elt/develop/ifw/IFW-24/ifw-fcf-6.0.0/sphinx/html/
PLC Libraries https://www.eso.org/projects/elt/develop/ifw/IFW-24/ifw-fcf-6.0.0/sphinx/html/docs/plc.html

## Slide 4: ELT Instrument Device Control
Embedded PC (PLC) – CX2033
Instrument WS
Device Manager (OPC UA Client)
Beckhoff
OPC UA Server
PLC App
HW
ADS
OPC UA
Win 10 IoT
EtherCAT
TwinCAT 3 PLC Runtime
Legend: Application to be developed
TwinCAT 3 IDE
ADS

## Slide 5: PLC Library Types
Compiled libraries *.compiled-library
    Commercial libraries with hidden source code
    Debugging is not possible
“Normal” libraries *.library
    ESO delivers this type
    Debugging is possible
Location: https://gitlab.eso.org/ifw/ifw-resource.git, folder PLC\libraries

## Slide 6: ESO PLC Library Concept

## Slide 7: Library Repository vs. Project References
Library Repository is where libraries are installed in TC3 IDE
Project References are libraries used in TC3 PLC project
Every TC3 IDE must install libraries in the Repository
Project References are added from TC3 Library Repository
GIT
Dev xxx
Lamp
Shutter
Motor
…
TwinCAT 3 IDE Library Repository
Dev xxx
Lamp
Shutter
Motor
…
PLC Project References
(Lamp + Motor + etc.)
Dev xxx
Lamp
Motor
Install
Add
Add
Add

## Slide 8: IFW PLC Library Versions
Library version is included in the library name.
This convention applies to all new library updates.
Examples:
    cryo_0.0.2.17.library
    Motor_4.2.6.0.library
    rsCommCommon_0.2.2.0.library

## Slide 9: Library Version Control
Library versions MUST be hard-coded in the TwinCAT project !!!

## Slide 10: Device Simulators
  Every FB has its own Simulator
    FB_ACTUATOR  FB_SIM_ACTUATOR
    FB_LAMP  FB_SIM_LAMP
    FB_MOTOR  FB_SIM_MOTOR
    FB_XXX  FB_SIM_XXX
  FB code doesn’t handle simulation
  FB_SIM_XXX simulates I/O, i.e., the response

## Slide 11: Logging

## Slide 12: GUI Templates
Every library provides GUI templates for supported devices.

## Slide 13: GUI Creation from Templates
Place a Frame on the canvas and select Visualization template.
Set the Reference to FB instance.

## Slide 14: GUI Example

## Slide 15: One GUI Fits All
MAIN.nPtrIndex := 1
MAIN.nPtrIndex := 2
MAIN.nPtrIndex := 3

## Slide 16: PLC Device States/Substates
Mandatory States: NOT_OP and OP
Mandatory Substates of NOT_OP
    NOT_INITIALISED
    INITIALISING
    READY
    ERROR
Mandatory Substates of OP
    ERROR
    Any specific substate, e.g., OPEN, OPENING, CLOSED, ON, OFF, etc.

## Slide 17: Actuator State Machine

## Slide 18: Motor State Machine

## Slide 19: PLC Device Data Model
FUNCTION_BLOCK FB_DEV
VAR
{attribute 'OPC.UA.DA' := '1'}
cfg: T_DEV_CFG; // Configuration structure (R/W)
{attribute 'OPC.UA.DA' := '1'}
ctrl: T_DEV_CTRL; // Control structure (R/W)
{attribute 'OPC.UA.DA' := '1'}
{attribute 'OPC.UA.DA.Access' := '1'}
info: T_DEV_INFO; // Info structure (R/O)
{attribute 'OPC.UA.DA' := '1'}
{attribute 'OPC.UA.DA.Access' := '1'}
stat: T_DEV_STAT; // Status structure (R/O)
{attribute 'OPC.UA.DA' := '1'}
{attribute 'OPC.UA.DA.Access' := '1’}
debug: T_DEV_DEBUG; // Debug structure (R/O)
// Outputs q_*
q_bSig1 AT %Q*: BOOL; // Digital OUT
q_nSig1 AT %Q*: INT; // Analog OUT
...
// Inputs i_*
i_bSig1 AT %I*: BOOL; // Digital IN
i_nSig1 AT %I*: INT; // Analog IN
...
i_nCouplerState AT %I*: UINT; // Link it to Coupler->InfoData->State
END_VAR

## Slide 20: RPC Calls
Simplify Interface to Linux Device Manager - OPC UA Client
Hide the complexity of the internals
Perform checks if command is possible (returns 0 = OK, -xxx = error)
Example: Move to Pos 70 with Velocity 5

## Slide 21: Mandatory RPC Calls
RPC_Reset # Reset Device
RPC_Stop # Stop Device
RPC_Init # Initialise device
RPC_Enable # Go to OP State
RPC_Disable # Go to NOT_OP/READY

## Slide 22: Local Control
Local Mode prevents high level commands while working in close vicinity to HW
Device Manager doesn’t send commands if device is in Local Mode
PLC GUIs control buttons are enabled only in Local Mode

## Slide 23: Supported Controllers
Actuator - Generic ON/OFF control
CCC - Cabinet Cooling Control, separate presentation by Claudio Reinero
Cryo - separate presentation by Dan Popovic
Cryohmi - Cryo interface to HMI (separate Cryogenic HMI presentation by Diego Del Valle)
ioDev - Sensors
Lamp
Motor
Piezo - Multi-channel analog piezo control
rsComm* - serial, Tcp/Ip, Tcp/Rt, MODBUS, RS_BASE, Lakeshore, …
Shutter
SmarAct - Modular control system for SmarAct piezo actuators
Timer - Time simulator & trigger synchronization
Utils - MUDPI Protocol

## Slide 24: Actuator Library – FB_ACTUATOR
FB for low-level control of actuators, e.g., power control.
Similar to FB_LAMP but HW state (On/Off) not affected by state change. The HW state can only be changed in OPERATIONAL state using ON and OFF commands.
Can be configured to go ON on PLC reboot or on RESET of the controller. Configured with input parameter in_bInitialState.
in_bAutoOp should be set to TRUE, i.e., OP on boot.
Configuration should be hard-coded in PLC program!
actuator(
in_sName := 'actuator’,
in_bAutoOp := TRUE,
in_bInitialState := TRUE);

## Slide 25: Timer Library
FB_TIME provides time services to other components running within the PLC, e.g., computation of absolute time.
Can use Local, PTP, NTP or Simulated time.
Must run at 1 ms cycle !!!
FB_TIMER provides synchronization signals with up to 1 µs accuracy.
Outputs mapped to DO with oversampling.

## Slide 26: Timer Library GUI Templates

## Slide 27: Motor Library – FB_MOTOR, etc.
FB_MOTOR
FB_SIM_MOTOR
FB_MA_BASE # for multi-axis tracking device
    FB_MA_ADC # 2-axis tracking device
    FB_MA_DROT # single axis tracking device
FB_ASTRO # TEL & MUDPI Simulator (simplified slalib in ST)
FB_DIGITAL_SIGNAL_FILTER

## Slide 28: FB_MOTOR Safety Related Input Params
New feature in Motor Library
  in_bSafe - Flag if safe to move the motor
  in_bDisableIfUnsafe - If unsafe, disable the motor
Motor is stopped when entering unsafe condition.
Motor is also disabled if configured to do so.
Once it is safe again, the control continues like nothing happened.

## Slide 29: Motor GUI Templates
GUI_TEMPLATE_MOTOR CONFIG
GUI_TEMPLATE_MOTOR CONTROL
GUI_TEMPLATE_MA_ADC
GUI_TEMPLATE_MA_DROT
GUI_TEMPLATE_ASTRO_CCS_SIM

## Slide 30: Motor Configuration GUI

## Slide 31: Motor Control GUI

## Slide 32: ADC GUI

## Slide 33: ASTRO GUI

## Slide 34: SmarAct Library
Modular Control System
High-precision piezo actuators.
Small form factor. Used where space is limited.
One HW controller, multiple channels (up to 18).
Tcp/Ip protocol.
Round-Robin fashion for control.
Too slow for multiple actuators.
HARMONI team implemented optimization. Thank you! To be implemented in the official library.

## Slide 35: SmarAct Controller MCS2

## Slide 36: SmarAct HW Configurations

## Slide 37: SmarAct FBs
FB_SMAR_ACT_BASE - SmarAct Ctrl App Talks to MCS2 ctrl. Must be EXTENDED.
FB_SIM_SMAR_ACT - SmarAct Ctrl App Simulator
FB_SA_CHANNEL_BASE - SmarAct single channel Ctrl.
FB_SIM_SA_CHANNEL - SmarAct single channel Simulator

## Slide 38: SmarAct GUI Template

## Slide 39: Tracking Library trklib
PLC C++ wrapper for slalib.
Not used in ELT.
CCS will send date using MUDPI protocol.

## Slide 40: Utilities
Currently includes only the MUDPI protocol.

## Slide 41
@ESOAstronomy
@esoastronomy
@ESO
european-southern-observatory
@ESOobservatory
Dan Popovic – dpopovic@eso.org