## Slide 1
END to END TRACKING DEMO
ELT ICS Seminar 2024
Mario Kiekebusch/Dan Popovic
Mauro
Ricardo

## Slide 2
Some Definitions …
Tracking devices are motorized functions which update continuously the position of one or more motor axes as a function of the telescope coordinates, time or variations of the temperature.
They support at least two modes of operations: one where motor axes are stationary and another one for tracking.
They may require a connection to the ELT time synchronization system.
The tracking device is sending a new set point at every cycle of the tracking loop. The period of the tracking loop is configurable and does not depend on the PLC cycle.

## Slide 3
Tracking State Machine

## Slide 4
Evolution
Tracking devices in VxWorks (reference implementation).
PLC re-implementation for VLT instruments.
PLC implementation for ELT (without CCS - as pointing kernel)
PLC implementation for ELT (with CCS)

## Slide 5
HW & SW Setup
Motor FB
Distributed Clock
EL6688 Process Image
Beckhoff NC Task
Derotator FB
CCS Receiver FB
PLC2
PTP time offset
Time FB
CCS data
via MUDPI
DC Time
Motor Status
Motor Control
Rotation
UTC time
PTP
Motion Controller
PLC1
Publisher
CCS Emulator
1Gb point to point
CCS data is extrapolated at each PLC cycle.
Rotation is used by the Derotator device during tracking.
Task Publishing at 20Hz.
It uses C++ modules for the CCS data generation (pointing kernel).
CCS Data is computed ahead of time (50ms).
It requires TwinCAT 3 TCP/UDP Real-Time (TF6311).
Time FB

## Slide 6
HW & SW Setup with ASTRO
Motor FB
Beckhoff NC Task
Derotator FB
PLC2
Time FB
DC Time
Motor Status
Motor Control
Rotation
Motion Controller
ASTRO
Distributed Clock

## Slide 7
CCS Deterministic Data

## Slide 8: DEMO

## Slide 9
@ESOAstronomy
@esoastronomy
@ESO
european-southern-observatory
@ESOobservatory
Luigi Andolfato; Diego Del Valle; Sylvie Feyrin; Arturo Hoffstadt; Mario Kiekebusch; Jens Knudstrup; Christoph Moins; Ivan Muñoz; Dan Popovic; Claudio Reinero; Calle Rosenquist; Paola Sivera; Ricardo Schmutzer; Piotr Szubiakowski