## Slide 1: Detectors in Astronomy
Alain Smette
System Scientist for VLT Instrumentation
ESO

## Slide 2
Introduction
Detectors based on photo-electric effect:
  CCD
  CMOS detectors
  MAMA & photo-multiplier tubes
Characteristics of CCD and CMOS detectors
Signal-to-noise ratio
FITS files
Summary

## Slide 3: Optical, near- and mid-IR observation
Science object
Atmosphere (optional)
Telescope
Instrument
Detector

## Slide 4: Disclaimer
This talk is only about UV, optical, IR photons detectors;
It does not describe radio detectors…
… neither neutrino, cosmic rays, nor gravitational wave detectors!

## Slide 5: Ideal detector
An ideal detector of light would record all information carried by each of the photons provided by the object/atmosphere/telescope/instrument system – and only them, with no loss, – within quantum uncertainty limits:
  Energy (wavelength, frequency)
  Polarization
  Phase
  Location of arrival on detector
  Time of arrival

## Slide 6: Different methods of detection. Retina: isomerization
Eye retina: absorption of one photon changes the structure of a molecule, which triggers a number of chemical reactions before a neuron signalling (http://www.ncbi.nlm.nih.gov/books/NBK22541/)
Biochemistry. 5th edition.
Berg JM, Tymoczko JL, Stryer L.
New York: W H Freeman; 2002.
Isomerization: process by which one molecule is transformed into another molecule which has exactly the same atoms, but the atoms have a different arrangement

## Slide 7: Different methods of detection. Photographic plate: chemical reaction
Photographic plates:
  Ag+Br- (crystal) + hv (radiation) → Ag+ + Br + e-
  Ag+ + e- → Ag0
  Chemical process to remove Br
Hardly used anymore in modern observatories

## Slide 8: Different methods of detection. (Current) astronomical detectors: photo-electric effect
Photo-electric based detectors
  Charge Coupled Devices (CCD): optical
  CMOS: infra-red, optical
  Multi-Anode Microchannel Array (MAMA): STIS, ACS, COS (UV)

## Slide 9
Introduction
Detectors based on photo-electric effect:
  CCD
  CMOS/IR detectors
  MAMA & photo-multiplier tubes
Characteristics of CCD and CMOS detectors
Signal-to-noise ratio
FITS files
Summary

## Slide 10: Absorption of photons in a semiconductor: Valence & Conduction Bands
In a crystal lattice, the allowed bands of electrons can be described by valence and conduction bands (similar to quantum orbits of electrons in Hydrogen).
valence band = "ground states" that are normally completely filled
conduction band = "excited states" that are normally completely unfilled, electron in the conduction band can move if there is electric field
electrons are either in a valence or in a conduction band
Dorn 2009

## Slide 11: Photo-electric effect in a semi-conductor
Parameters: Quantum Efficiency (QE) , Dark current
QE =
Dark level: # of thermally excited electrons which reached the conduction band

## Slide 12: A. Charge Coupled Device (CCD) & variations
Animation by Michael Schmid

## Slide 13: A. Charge Coupled Device (CCD) & variations
Parameters: full-well capacity, bias level, gain, ADC saturation level
Gain: ⚠ g = number of ADUs/electron or number of electrons/ADU (g = 1/CONAD)
Full well capacity: maximum # of photo-electrons in a pixel
Bias level: artificial electronic offset which ensures that the ADC always receives a positive signal.
ADC saturation level: # of bits used by the A/D converter is: 16 bits -> 65 535 ADUs
amplifier
Analog-to-Digital Converter : Converts charges to ADU

## Slide 15: Pre-/post-/over-/under- scan regions
Regions not exposed to light: pseudo-pixels generated by sending additional clock cycles to the output electronics

## Slide 16
One of the 2 CCDs used in ESPRESSO:
81 millions pixels

## Slide 17
OmegaCAM detector array:
32 2048x2048 detectors;
268 millions pixels

## Slide 18: B. Hybrid Complementary Metal Oxide Semiconductor (CMOS) detectors

## Slide 19: B. Hybrid Complementary Metal Oxide Semiconductor (CMOS) detectors
Dorn 2009
Charge diode capacity by reverse bias voltage
Floating capacity is discharged by absorbed photons
Read voltage across diode capacity by addressing unit cell source follower
Each pixel is read individually.
Each pixel can be read multiple times during an exposure.
Exposure time is reported as DIT. A file usually includes the average of NDIT individual exposures.
Parameters: full-well capacity, gain
Full well capacity: maximum # of photo-electrons in a pixel
Gain: g = number of ADUs/electron

## Slide 20: B. Hybrid Complementary Metal Oxide Semiconductor (CMOS) detectors
De Groof et al. 2008
The signal lifetime in the pixel: reset to black level (high voltage V DD : yellow), photocharge integration (dropping voltage: green), and voltage readout (red).

## Slide 21
Mosaic of 16
2048x2048 CMOS detectors used in VIRCAM

## Slide 22: Comparison: CCD vs CMOS
Requires a shutter
Usually, no need for a shutter

## Slide 23: C. Multi-Anode Microchannel Array (MAMA)

## Slide 24
Introduction
Detectors based on photo-electric effect:
  CCD
  CMOS/IR detectors
  MAMA
Characteristics of CCD and CMOS detectors
Signal-to-noise ratio
FITS files
Summary

## Slide 25: Behavior relative to ideal detector (for optical, near- and mid-IR astronomy)
Energy:
  Broad band sensitivity
  Need for filters or
  spectrograph
Polarization: N/A: need for polarization optic
Phase: N/A: specific optics; interferometry
Dorn 2009

## Slide 26: Behavior relative to ideal detector (for optical, near- and mid-IR astronomy)
Time of arrival:
  MAMA: Time-tag to each individual photon individually
    But not too many photons can arrive at the same time!
  CCDs: time associated with each exposure
    Limited by the read-out time
    Most CCDs tuned to faint target observations leading to long read-out time;
    Can be windowed
    Trick: move charges in a direction while integrating
      HIT mode on FORS
      Time delay and integration to match sidereal rate for fixed telescopes
  CMOS detectors: time associated with each exposure
    limited by the read-out time, but faster then CCD
    ‘burst’ mode can allow to save each frame
    pixels are often read one after the other

## Slide 27: Behavior relative to ideal detector (for optical, near- and mid-IR astronomy)
One electron for each photon?
  Linearity
    Behavior at low/high flux: see next slides
    Pixel-to-pixel variation (also called fixed pattern noise)
    Fringing
    Charge transfer efficiency
  Are there electrons not associated with incoming photons?
    Bias level
    Hot columns/rows, hot pixels, traps…
    Dark current
    Radiation events (‘cosmic rays’)
    Read-out noise
    Quantization noise

## Slide 28: Behavior relative to ideal detector (for optical, near- and mid-IR astronomy)
Linearity
  MAMA: good behavior at low flux only, otherwise pile-up
  CCD:
    old CCDs (1980’s…) were not linear at low flux: they needed to be ‘flashed’. Solved in current CCDs.
    good behavior in general
    saturation when approaching the full well capacity
    pixel-to-pixel variation caused by small differences between pixels
  CMOS detectors: intrinsically non-linear, as accumulation of charges changes bias on detector for simple readout
    more complex readout electronics (up to 70 transistors per pixel!)
    pixel-to-pixel variation (fixed-pattern noise): mostly caused by small difference between electronics assigned to each pixel

## Slide 29: CCD Linearity
This graph and following: from http://www.eso.org/sci/facilities/develop/detectors/optdet/instruments.html

## Slide 30: CCD Linearity
OmegaCAM, detector #84 ‘Centaurus’

## Slide 31: CCD linearity
Different quantities:
ADC saturation level: set by the Analog/Ditigal Converter.
(here: 15 bits: 2^15 = 32767)
Full-well capacity: physical limit set by the characteristics of the pixel; usually higher than ADC saturation level
Linear range: range within which the CCD responds linearly within a given level (say 1%)

## Slide 32: Photon transfer curve
Take 2 images with same illumination levels
Change illumination level
Make difference
Measure variance
Report vs signal
Slope is gain of the ADC converter
Dorn 2009

## Slide 33: Pixel-to-pixel variation; fringing

## Slide 34: Bias level, hot columns, pixels
bias
3600s dark
Zoom on dark

## Slide 35: Defects: bad columns, traps, ‘stuff’, saturation, blooming
https://www.eso.org/~ohainaut/ccd/CCD_artifacts.html

## Slide 36: Radiation events (‘cosmic rays’)
Smith et al. 2002, SPIE 4669, 172

## Slide 37: Radiation events

## Slide 38: Charge Transfer Efficiency (CTE)
Fraction of electrons that are successfully moved from one pixel to another during read-out
  Charge Transfer Inefficiency: CTI = 1 - CTE
Values can differ between parallel and serial readout: E.g.: OmegaCAM CENTAURUS:
    Serial: 1
    Parallel: 0.9999995 (1 charge loss every 1000 for a pixel at row 2048)
Degrades due to radiation:
  in particular, affects space instruments
  depends on signal level

## Slide 39: CTI evolution for HST/STIS CCD
Goudfrooij, P., Wolfe, M. A., Bohlin, R. C., Proffitt, C. R., and Lennon, D. J., 2009,
“STIS CCD Performance after SM4,” Instrument Science Report STIS 2009-02.

## Slide 40: Sources of noise
Read-out noise (RON):
  Noise produced by the electronics of the amplifier
  Follows a gaussian distribution
Thermal noise: thermal excitation of electrons in valence band
  origin of dark current, reason to cool detectors
  Poisson distribution
kTC noise in CMOS/IR detectors: reset voltage is not always constant
  Usually dealt with by readout mode
Quantization noise (QN):
  Analog-to-digital converter (ADC) converts electrons to ADUs
  16-bits ADCs produced a max of 2^16 = 65 535 ADUs
  ADC only outputs discrete levels: range of analog inputs can produce same output: round-off error is quantization noise
  QN = 1/sqrt(12) ADU

## Slide 41: CMOS (IR) detectors read-out mode
Dorn 2009

## Slide 42: CMOS (IR) detectors read-out mode
Dorn 2009

## Slide 43: RON decrease using Fowler-sampling

## Slide 44: Source of noise
1/f, pink noise, flicker noise: affects a number of electronics, origin not well understood
  Noise behaving as , (f = read-out frequency)
    often close to 1
  Consequence: SNR does not increase with # of integrations
  Usually not relevant in modern detectors
  Unfortunately affects AQUARIUS arrays: VISIR, MATISSE, JWST/MIRI
    For VISIR, requires high chopping frequency

## Slide 45: Behavior relative to ideal detector (for optical, near- and mid-IR astronomy)
Location of arrival of photons on detector
  Pixel size is often chosen as to satisfy the Nyquist sampling criterion (2 pixels/resolution element)
  However, different problems can occur:
  CCD:
    Coating can increase the FWHM of the PSF
    Bad clocking pattern
    Lateral charge diffusion
    Thickness combined with a
      fast camera
    For space instrument:
    Significant CTE leads to shift of
    PSF centroid.

## Slide 46: Behavior relative to ideal detector (for optical, near- and mid-IR astronomy)
CMOS (IR) detectors:
  Interpixel capacitance
    affects the point-spread function
    affects the determination of the gain
Finger et al 2006, SPIE 6267

## Slide 47
Introduction
Detectors based on photo-electric effect:
  CCD
  CMOS/IR detectors
  MAMA & photo-multiplier tubes
Characteristics of CCD and CMOS detectors
Signal-to-noise ratio
FITS files
Summary

## Slide 48: Signal-to-noise ratio
SNR =
Signal = object detected photons = (t)
Noise = σ =
  Variance from
    Photon noise: (in electrons)
      object: object detected photons = (t)
      sky: sky detected photons =
      thermal background: background detected photons =
      detector dark current: dark current rate =
    Read-out noise: in electrons
    Quantization noise:
    Other noise: can often be corrected (if enough care taken during calibrations)

## Slide 49: Signal-to-noise ratio
SNR =
Different regimes:
  Read-out noise limited:
    faint target, little sky
    RON contribution larger all other contributions
    Exposure should be as long as possible: limited by radiation events, observing constraints
  Photon noise limited:
    bright target, bright sky (extreme case: mid-infrared imaging from ground), large thermal background, dark current (UV in space)
    little affected by number of exposures:
      trade-off with overheads associated with individual exposures

## Slide 50: Signal-to-noise ratio
Object photon noise limited: SNR =
RON limited: SNR =
Background limited
  SNR = (X is either S, B, D)
  Often limited by systematics affecting the determination of the background or the determination of

## Slide 51: Special case of mid-infrared wavelengths
VISIR User Manual
Number of photons from sky and telescope is larger than number of photons from the object (>> ) !
Very short exposure times (~ 10 ms)
Synchronization of detector reading with chopping (~ Hz motion of a mirror in the light path – such as M2)

## Slide 52
Introduction
Detectors based on photo-electric effect:
  CCD
  CMOS/IR detectors
  MAMA & photo-multiplier tubes
Characteristics of CCD and CMOS detectors
Signal-to-noise ratio
FITS files
Summary

## Slide 53: Flexible Image Transport System (FITS) files
Widely used format for transporting, analyzing and archiving astronomical images. Much more than just a format.
  Primarily designed to store scientific data sets of multidimensional arrays (images) and 2-dimensional tables organized into rows and columns of information
Endorsed by ESO, NASA and the International Astronomical Union (Vatican Library, …)
Header keywords provide descriptive information about the data:
  Site, Telescope, Instrument and Detector information
  World Coordinate System parameters
Header keywords and data format follow a (strict) standard

## Slide 54: FITS file
A FITS file is comprised of segments called Header/Data Units (HDUs),
  First HDU is called the `Primary HDU', or `Primary Array’:
    can contain a 1-999 dimensional array of 1, 2 or 4 byte integers or 4 or 8 byte floating point numbers using IEEE representations.
    typically a 1-D spectrum, a 2-D image, or a 3-D data cube.
  Any number of additional HDUs may follow the primary array: FITS `extensions'. Types of standard extensions are currently defined:
    Image Extensions contain a 0-999 dimensional array of pixels, similar to a primary array (header begins with XTENSION = 'IMAGE ')
    ASCII Table Extensions store tabular information with all numeric information stored in ASCII formats (header begins with XTENSION = 'TABLE ')
    Binary Table Extensions store tabular information in a binary representation. Each cell in the table can be an array but the dimensionality of the array must be constant within a column. (header begins with XTENSION = 'BINTABLE')

## Slide 55
First entries in a FITS Primary HDU header:
Data types in an image array:
8-bit (unsigned) integer bytes
16-bit (signed) integers
32-bit (signed) integers
32-bit single precision floating point real numbers
64-bit double precision floating point real numbers

## Slide 56: Summary
Bias
Read-out noise (RON)
Dark level
Quantum efficiency (QE)
Full-well capacity
Gain (g); pixel-to-pixel variation, fixed-pattern noise
ADC saturation level
Linearity
Exposure time; DIT/NDIT
Fringing
Charge Transfer Efficiency (CTE)
Detector defects: bad/hot columns; hot pixels.
Radiation events ‘cosmic rays’