## Slide 1: MAORY design trade-off study: tomography dimensioning
Sylvain Oberti, Miska Le Louarn – ESO Garching
Emiliano Diolaiti, Carmelo Arcidiacono, Laura Schreiber, Matteo Lombini – INAF Bologna
and the rest of the MAORY consortium
AO4ELT5 – Tenerife – 30-06-2017
Notes: I am Sylvain Oberti, working for ESO but contributing to the MAORY consortium
I am sorry to bother you during the digestion process.
Sorry for the misleading title.

## Slide 2: Multi-conjugate Adaptive Optics RelaY for the E-ELT
MAORY serves MICADO
+ future second port INS (TBD)
Notes: MAORY stands for Multi-conjugate Adaptive Optics Relay for the E-ELT.
It serves the instrument MICADO, a 1’ imager + spectrometer
+ future 2nd port TBD

## Slide 3: Outline: phase B design trade-off
1- Analysis of dimensioning parameters constrained by tomographic and generalized fitting error
  Number of post-focal DMs conjugated in altitude
  DM pitch
  DM altitudes
  LGS asterism angle
  Number of LGS
  LGS and NGS asterism geometry - not shown in this talk
under some constraints
  Seeing
  Cn2 profile
  Zenith distance
  Telescope phase 1 / phase 2
    Number of LGSs: 4/6
    M1 central obstruction: 28%/57%
2- LGS WFS design: new concept of super-resolution wavefront sampling, a way to improve multi WFS AO and get rid of spot truncation
Notes: Revisit phase A design !
Main purpose of this recent study is to address high level trade-off related to tomography and fitting error, essentially DMs TLRs and LGS number and asterism angle. This is done under constraint of external parameters: seeing, Cn2, phase 1/phase 2
I will show some analyses, compare baseline to other options and open discussion

## Slide 4: Driver: MAORY main specifications
Performance in best conditions
  Q1 seeing (0.234 m) and wind, as close to zenith as possible
  Over 20” FoV
  SR > 50% @ 2.2 microns (goal 60%)
  Sky coverage requirement not applicable
Performance in median conditions
  median seeing (0.157 m) and wind, as close to zenith as possible
  Over 1’ FoV
  SR > 30% @ 2.2 microns (goal 50% @ 2 microns)
Performance in sub optimal conditions
  Q3 seeing (0.139 m) and wind, zenith distance 30 degrees
  Over 2’ FoV
  SR > 15% @ 2.2 microns (goal 30%)
SR uniformity < 10% absolute PTV across FoV of interest
Sky coverage > 50%
Notes: Error budget MAORY 231 nm, telescope 145 nm rms  37% SR en K
Main spec: Focus on median and sub optimal conditions which are the design drivers

## Slide 5
  Simulated MCAO WFE terms
  Generalized fitting
  Spatial aliasing
  Temporal error
  LGS WFS noise
  NGS WFS noise
  Tomographic error
  Command computation:
  Tomographic reconstruction to estimate the multi layer turbulent phase: FRIM3D/POLC with perfect priors on Cn2 profile
  Projection of the estimated 3D phase onto the DMs space. The projection is optimized on a specific FoV
  No other error budget term
OCTOPUS® end-to-end simulation
  high flux and no spot elongation
  high flux
  cone effect and anisoplanatism but optimal reconstruction of 35 layers
Notes: For this reason, we are working without LGS spot elongation and with high flux for LGS and NGS. The reconstruction prior are perfectly known.
Star map to measure Sr across a FoV of 2’ square: 29 stars with a denser mapping around the center
6 LGS @ 1 ‘ off axis unless otherwise specified
3 NGS @ 70” off axis to split the technical field in two equivalent areas
4 tomography optimization field, actually acting on the projection of the reconstructed layers:
Full field
FoV1 for MICADO small field
FoV2 for MICADO large field
FoV3 for 2’ field
3 turbulence profiles:
Spec
Jet stream @ 13.5 km
Worst case with intermediate layer @ 8.5 km
2 seeing and zenith angle cases: mentionned in blue in the following slides

## Slide 6
Typical simulated FoV
MICADO large field 53”x53”
MICADO small field 20”x20”
Notes: For this reason, we are working without LGS spot elongation and with high flux for LGS and NGS. The reconstruction prior are perfectly known.
Star map to measure Sr across a FoV of 2’ square: 29 stars with a denser mapping around the center
6 LGS @ 1 ‘ off axis unless otherwise specified
3 NGS @ 70” off axis to split the technical field in two equivalent areas
4 tomography optimization field, actually acting on the projection of the reconstructed layers:
Full field
FoV1 for MICADO small field
FoV2 for MICADO large field
FoV3 for 2’ field
3 turbulence profiles:
Spec
Jet stream @ 13.5 km
Worst case with intermediate layer @ 8.5 km
2 seeing and zenith angle cases: mentionned in blue in the following slides

## Slide 7
Cn2 profiles
+ other profiles measured by stereo scidar
Notes: 3 turbulence profiles:
Spec
Jet stream @ 13.5 km
Worst case with intermediate layer @ 8.5 km

## Slide 8: Gen. fitting: N DMs and pitch
  2 post-focal DMs: performance flat for pitch < 1.5 m
  1 post-focal DM: performance flat for pitch < 2 m
  Strong impact from Cn2 profile
r0=0.129 m, Z=30º
Notes: 0.8” seeing Zenith=30
Plot shows min, max and averaged performance across 2 ‘ field vs. projected DM pitch in m on sky for:
1 post-focal DM (Right) vs. 2 post-focal DMs (Left)
Profile1 vs. Profile2
Conclusions:
- Pitch smaller than 1 m does not make sense for 2 post-focal DMs
- Pitch smaller than 1.5 m does not make sense for 1 post-focal DM
Strong impact of turbulence profile : dominates over the trade-off number of DMs and pitch  realistic Cn2 sensitivity analysis to be performed
In this case, with a layer @ 13.5 km, 1 DM case is not more sensitive than 2 DMs

## Slide 9: Benefit 2 vs. 1 post-focal DM(s)
  2 post-focal DMs desirable to increase sky coverage
  2 post-focal DMs provide performance improvement of up to 25% in the science field and 100% in the technical field in K band, 250% in J band
K band: 2.2 µm
r0=0.129 m, Z=30º
Notes: Gain in Sr 2 post-focal DMs vs. 1 in the following cases:
Top: Median seeing Z=30: Profile 1 vs. Profile 2 – optimization full field – different pitch
Bottom : Good seeing, Z=0, Profile 1 vs. Profile 3 – 3 fields for optimization of the projection – 2 pitches
MICADO large field diagonal is the red line
Conclusions:
2 post focal DMs provide performance improvement of up to 25% in the science field
Strong advantage in the technical field: up to factor 2 in K, 3.5 in J band
The message here is that 2 post-focal DMs are desirable in order to increase sky coverage
It could also be attractive for a future instrument: 2nd port

## Slide 10: Benefit 2 vs. 1 post-focal DM(s)
  2 post-focal DMs improve tolerance to Cn2 profile variation
Notes: Now, if we a look at a kind of worst case altitude turbulence layer w.r.t. to the ESO median profile, clearly 2 post-focal DMs are more robust to Cn2 change.

## Slide 11: E-ELT phase 1 / phase 2 – J band
  M1 doughnut impact on Sr is not significant. How about NGS sky coverage ?
  Dramatic impact 6 LGSs  4 LGSs
  Lower wavelength performance pushes for:
    6 LGSs
    2 post-focal DMs
    finer DM pitch
Photon noise σ2
x3.8 long axis
K band: 2.2 µm
r0=0.129 m, Z=30º
Cn2: Profile 1
Notes: Study of E-ELT phase 1 / phase 2 impact on J band LE Sr averaged across the 2’ FoV
J band matters both for NGS sensing and science
3 cases:
- Left: E-ELT phase 2 with 6 LGSs and 28% central obstruction
Right: E-ELT phase 1 with 4 LGSs and 57% central obstruction
Middle: Hybrid case with 57% central obstruction and 6 LGSs
Conclusions:
Limited impact of doughnut on Sr but on sky coverage: To be analysed
Strong impact of number of LGS
Benefit from having 2 post-focal DMs: limited in phase 1, yes with 6 LGSs
6 LGSs is a must have !

## Slide 12: Post-focal DM altitude: single DM
  1 post-focal DM: conjugation altitude matters and should be > 14 km
  The conjugation altitude should be higher to cope with larger airmass cases
K band: 2.2 µm
r0=0.129 m, Z=30º
Cn2: Profile 1
Notes: 0.8” seeing Zenith=30
Plot shows orthodadial averaged Sr vs star radial position in the field
Conclusion:
With 2 DMs, performance is not sensitive to lower DM altitude
With 1 DM, altitude should be higher than 12 km
Altitude of higher altitude DM not analyzed in the 2 DM case, Action ?
Baseline is, since phase A, to have the DMs @ 4 km and 12.7 km
To be robust to higher airmass, I propose to put the DMs at higher altitude (maybe 6 and 15 km ?). The turbulent layer are shifted upwards linearly with airmass, so factor of 2 at Z=60
Of course, this needs to be confirmed by a cn2 sensitivity study

## Slide 13: Post-focal DM altitude: 2 DMs case
  Results confirmed by Cn2 sensitivity study
  Performance insensitive to DM1 altitude
  DM2 optimal altitude naturally increases with airmass
  16 km conjugation is a good trade-off
  16 km is also close to optimal for a single post-focal DM  Upgradability
Notes: Performance shown in the MICADO large field and full field, with 2 DMs pitch 1.5m, playing with DM1 and DM 2 altitudes
16 km is a good choice valid for both cases where we use a single or two post-focal DMs
Cn2 sensitivity studies confirm these altitudes: not very sensitive

## Slide 14: LGS asterism angle – full field optim
  Tomography reconstruction maximizes performance in full field here
  Closer LGSs improve Sr on axis, decrease uniformity across the MICADO field and decrease the Sr in the technical field
  Trade-off between 45” and 1’ radii  other FoV optimization to check
K band: 2.2 µm
r0=0.129 m, Z=30º
Cn2: Profile 1
1’ radius
45”radius
Notes: This is performance against field position for different LGS radius
LGS asterism with full field optimisation of the projection
Important to say that tomography is optimized in full field
Closer LGSs improve the Sr on axis but decrease uniformity and Sr in technical field
Trade-off between 45” and 1’ radii
We can combine LGS asterism angle tuning and SW reconstruction tuning

## Slide 15: LGS angle – projection optimization
  Tomography reconstruction maximizes performance in 3 different FoVs with NGS @ 70” off axis
  Maximum and average Sr in MICADO field highest for LGS @ 45” off axis
  Average performance in 2’ FoV highest for LGS @ 1’ off axis
  Baseline: 45” radius
K band: 2.2 µm, r0=0.157 m, Cn2: Profile1
Notes: Same analysis as performed before but for spec seeing (0.6”) pitch of 2m and different optimal fields for 2 zenith angles
For LTAO optimal angle ranges between 45” at zenith and 20” @ Z=60
The larger the zenith angle the closer the LGSs should be.

## Slide 16: Ultimate performance in 20” square
  Best performance on axis (LTAO with on axis NGS) is achieved with 20” radius @ Z=60
  NGS cannot be closer than 30” radius without vignetting the science FoV
  Confirmation that a fixed 45” radius is almost optimal for MICADO at any airmass for both small field and wide field: one single asterism configuration  less complexity
Notes: @ large airmass the NGS correction was too poor when optimizing on axis and forced to enlarge the FoV on=f the NGS WFS  too long computation.
Here noi NGS, all mods corrected by the LGS, this helps even more the perf on axis.
At Z=60 one can see the performance
- on axis
- in MICADO small FoV
in MICADO large field
On axis, as in LTAO, optimal radius is 20”
In MICADO small FoV, going down to 30” radius provides a significant performance improvement
In any case, 45” is the best case for any zenith distance when it comes to performance in the large MICADO FoV.
45” is a hard limit with pick-off mirrors, could be decreased with prisms
Shall we try to decrease the hard limit of asterism angle ? Is it a significant performance improvement for MICADO @ Z=60? We should ask Rick probably

## Slide 17: Conclusions on design trade-off
  2 post-focal DMs (baseline: 1) are desirable in order to enhance:
    Performance in the technical field  sky coverage and robustness (acquisition)
    Performance in the blue for NGS sky coverage and MICADO performance
    Robustness to Cn2 profile variation and zenith distance
  DM pitch between 2m and 1.5m  better for worse seeing and with 2 DMs
  Post-focal DMs altitude: 4-6 and 16 km to be robust to larger airmass and accommodate 2 post-focal DMs later
  LGS asterism angle: fixed @ 45” radius + optimization of tomography projection depending on FoV of interest
  E-ELT phase 1 / phase 2:
    M1 doughnut main impact on sky coverage and PSF shape: TBC
    6 LGSs are highly desirable
Notes: Main choices:
2 post-focal DMs should be pushed but baseline is 1
Pitch 1.5 m preferred
DM altitude 16 km for highest and flexible for lowest
6 LGSs are a must

## Slide 18: WF sampling super-resolution
Notes: New idea based on the concept of super-resolution:
- A frozen scene can be super resolved by stacking undersampled frames shifted by a fraction of sampling element

## Slide 19: WF Super-resolution: rationale
  Current MAORY design is based on 6 LGS WFS with 80x80 subapertures and 10x10 pixels of 1” to 1.5” per subaperture
  Spot truncation occurs as spot elongation can get as large as 25”: why not reducing the number of subapertures and increase the number of pixels per subaperture ?
  Why we could live with less subapertures ?
    We have a redundant multi WFS system
    Altitude turbulence is weak
    The spatial sampling in altitude can be coarser
    MAORY altitude DMs baselined with pitch of 1.5 to 2m: can be easily controlled with subapertures of pitch > 0.5 m
  Problem: How to sample the ground layer properly to be able to control 5000 degrees of freedom provided by M4 ?
    Break the symmetries by not aligning the WFS with the pupil
    Go for super-resolution wavefront sampling thanks to sub-sample shift
    The ground layer and possibly the DM is seen the same way by all WFS

## Slide 20: Basic monodimension description
Sampling with a grid of sampling period T and subaperture (or sampling element) size T across which the signal is averaged out
Let S be the function describing the 1st derivative of the wavefront along one axis (a line across the pupil). The concept can be generalized by considering S to be the phase or its second derivative or an intensity pattern in the focal planem or elsewhere, etc …
x
amplitude
S(x)
T
Sampling with same resolution but grid shifted by half a sampling element
T
T/2
Combining the 2 sampling patterns (blue and red), we effectively get a twice smaller sampling period T/2 but keeping a subaperture size of T
Notes: Basic monodimensional description

## Slide 21: Combining sampled measurements
=
  By concatenating the sampled measurements in the direct space from blue and red cases, we get:
  A sampling period T/2  the same spatial resolution but a twice wider first null point of the sinc function hence better sensitivity
FT
Sensitivity function remains the same
Only related to subaperture size
The sampling period is twice larger.
The distance between the diracs is wider in frequency domain
aliasing is reduced
Notes: Combining sampled measurements consists of:
Convolution of the spatial function by a top hat
Multiplication by a sum of 2 shifted dirac comb, which provide another dirac comb with a twice smaller period
In Fourier space:
Sensitivity function that depends only on subaperture size and shape
Convolved to a Dirac comb with twice better spatial resolution and a reduced aliasing

## Slide 22: First numerical simulations
  VLT case – 8 m – AOF dimension
  1364 KL modes in the pupil plane
  Modal interaction matrices:
    1 40x40 SH
    5 co-aligned 20x20 SH
    5 20x20 SHs with pupil shift of +/- 50% SA in X and Y
    5 20x20 SHs with pupil rotation of 0, 11, 22, 33 and 44 degrees
  Analysis of spatial frequency contained in the signal by singular value decomposition
  Noise propagation
  Wavefront reconstruction
  Tomography case with 4 LGS WFS @ 10” off axis (LTAO)
Notes: Some simulation:
Modal IM
Minimum variance open loop reconstruction error
Tomographic case

## Slide 23: Singular value decomposition
Information at all spatial frequencies retrieved by shifted and rotated SHs

## Slide 24: Noise propagation
High noise propagation with shifted SH because of bad management of edge effects, while rotated SHs propagate more noise than 40x40 along the high order modes due to sensitivity penalty

## Slide 25: WF reconstruction with unknown DM model shift (4cm in M1 space)
The rotated 20x20 case behaves like the 40x40 case
In both cases, we can reconstruct ~ 1300 modes, where the WFE becomes as large as the input WF

## Slide 26: Monolayer reconstruction with MV

## Slide 27: LGS tomographic reconstruction open loop minimum variance
The shifted 20x20 case performs well across the first 2 km altitude
Then, superresolution is built in for all cases which behave similarly

## Slide 28: WF sampling by a grid
Classically, SH WFS are designed with a square grid of subapertures with the following assumptions:
  Regular spacing of the subaperture (dirac comb sampling)
  Sampling period equal to subaperture size (top hat)
The SH measurement operator in Fourier space is:
Combining geometrically 4 SHs shifted by half a subaperture in X and Y can be considered as a meta SH WFS with:
  Regular spacing of the subaperture (dirac comb)
  Sampling period twice shorter  less aliasing
  Same subaperture shape and size  same sensitivity
This way, we can decouple the subaperture size from the sampling period in our designs
Subaperture size
Sampling period
Sensitivity function
Sampling function
T=d/N

## Slide 29: Benefit and next steps
  For MAORY, going to 40x40 subapertures would bring the following obvious benefits:
    20x20 pixels per subaperture  no truncation and better linearity
    Flux per subaperture x 4
    RTC MVM complexity ~ /4
  Super-resolution seems well suited for wide field AO, e.g. 7’ NGS GLAO mode with few subapertures (20x20 ?)
  Multi WFS AO systems may not want to correct misregistrations but just measure them accurately
  Next steps:
    Aliasing reduction: analytical evaluation
    End-to-end model for MAORY and trade-off on subaperture number
    Try to find why it does not work …

## Slide 30: Thank you for your attention !